## Slide 1: Computer Organization Homework 1

## Slide 2: Procedure Calling
Steps required
  Place parameters in registers
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call

## Slide 3: Register Usage
$a0 – $a3: arguments (reg 4 – 7 )
$v0, $v1: result values (reg 2 and 3)
$t0 – $t9: temporaries (reg 8 – 15, reg 24 and 25)
$s0 – $s7: saved (reg 16 – 23 )
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)
$sp
0x4005
0x4002
0x4004
0x4003
0x4000
0x4001

## Slide 4: Procedure Call Instructions
Procedure call: jump and link
jal Procedure Label
  Put address of following instruction in $ra
  Jumps to target address
Procedure return: jump register
jr $ra
  Put the value of $ra in program counter
  Can also be used for computed jumps
    e.g., for case/switch statements

## Slide 5: Recursive Procedure Example
C code:
int fact (int n) { if (n < 1) return f; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0

## Slide 6: Recursive Procedure Example
MIPS code:
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1:
addi $a0, $a0, -1 # else decrement n jal fact # recursive call lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return

## Slide 7: QtSpim
Single Step
Assembly
Register
Load file
Run
7
下載網址:http://sourceforge.net/projects/spimsimulator/files/ 版本 9.1.20